B.E / B.Tech. PRACTICAL END SEMESTER EXAMINATIONS, APRIL / MAY 2019

Fourth Semester

CE8381 & STRENGTH OF MATERIALS AND FLUID MECHANICS & MACHINERY LABORATORY

(Regulation 2017)

Time : 3 Hours			       Answer any one Question	                      Max. Marks 100

| Aim/Principle/Apparatus required/Procedure | Tabulation/Circuit/Program/Drawing | Calculation & Results | Viva-Voce | Record | Total |
| --- | --- | --- | --- | --- | --- |
| 40 | 20 | 20 | 10 | 10 | 100 |

| Q.No. |  |
| --- | --- |
| 1. | Conduct a tensile test on a mild steel specimen and determine the following. (i) Limit of proportionality (iv) Ultimate strength (ii) Elastic limit (v) Young’s modulus of elasticity (iii) Yield strength (vi) Percentage elongation |
| 2. | Find the shear strength of the given specimens (Mild steel and Aluminium) using double shear method . |
| 3. | Perform the torsion test on the given specimen to find the following 1. Modulus of rigidity 2. Shear stress. |
| 4. | Conduct Rock well hardness test on mild steel, carbon steel, brass and aluminium specimens. |
| 5. | Conduct the load test on mild steel beam and determine the deflection and young modulus of the beam section in the specimen. |
| 6. | Find the stiffness and rigidity modulus of the given open coiled helical spring. |
| 7. | Find out the improvement in mechanical properties by comparing Quenched and Tempered Specimen with quenched specimen. |
| 8. | Determine the mechanical properties of the given specimen (at least two samples to be given for each material) before and after hardening. |
| 9. | Examine the given specimens through microscope (before and after hardening) and draw the diagrams. Also comment on the effect of hardening based on the microscopic examination. |
| 10. | Find the strain measurement of given rod by using Rosette strain gauge |
| 11. | Determine the Rockwell hardness no. of the given specimens. (i) Brass (ii) Mild steel (iii) Cast iron |
| 12. | Determine the Co-efficient of discharge(Cd) of a Venturimeter in 25mm Diameter of the pipe |
| 13. | Determine the efficiency of Kaplan turbine and draw the performance Characteristic curves |
| 14. | Determine the Co-efficient of discharge through an Orifice by Variable Head Method |
| 15. | Determine the maximum efficiency and draw the performance characteristic Curves by using Single Stage Centrifugal Pump. |
| 16. | Determine the maximum efficiency and draw the performance characteristic Curves by using Reciprocating Pump |
| 17. | Determine the Efficiency of the Francis turbine and draw the following Characteristic curves. a)Speed Vs Output power b)Speed Vs Efficiency |
| 18. | Carryout an experiment to determine the friction factor when the fluid flows Through the pipe. |
| 19. | Determine the efficiency of Pelton wheel and draw the performance Characteristic curves |
| 20. | Determine the maximum efficiency and draw the performance characteristic Curves of Gear Pump. |
| 21. | Determination of rate of flow by using Rota meter |