B.E / B.Tech. PRACTICAL END SEMESTER EXAMINATIONS, APRIL / MAY 2019

Fourth Semester

CE8381- STRENGTH OF MATERIALS AND FLUID MECHANICS & MACHINERY LABORATORY

(Regulations 2017)

Time : 3 Hours			       Answer any one Question	                      Max. Marks 100

| Aim/ Apparatus required | Procedure / Drawing/ Observation | Tabulation & Calculation | Graphs & Results | Viva-Voce | Record | Total |
| --- | --- | --- | --- | --- | --- | --- |
| 15 | 30 | 20 | 15 | 10 | 10 | 100 |

| 1. | Conduct a tension test on given mild steel specimen for finding the following: Yield stress Ultimate stress Nominal breaking stress Actual breaking stress Percentage Elongation in length Percentage Reduction in area. |
| --- | --- |
| 2. | Determine the impact strength of the given specimen by conducting charpy impact test. |
| 3. | Determine the maximum shear strength of the given bar by conducting double- shear test. |
| 4. | Determine the Rockwell hardness number for the given specimen. |
| 5. | Find the stiffness, rigidity modulus, shear stress and strain energy stored in the given helical spring. |
| 6. | Find the values of bending stresses and young’s modulus of the material of a beam (say a wooden or steel) simply supported at the ends and carrying a concentrated load at the center. |
| 7. | Conduct torsion test on mild steel round rod and determine the value of modulus of rigidity and maximum shear stress. |
| 8. | Find the brinell hardness number of tempered metals and hardened material. |
| 9. | Examine the microstructure of a given plain carbon steel sample before and after heat treatment. |
| 10. | Determine the stress & strain using strain gauges mounted on cantilever beam |
| 11. | Perform an experiment to determine the flow in a pipe using venturimeter and draw the calibration curves. |
| 12. | Conduct an experiment to determine the Co-efficient of discharge (Cd) of a Orificemeter for the given pipes. |
| 13. | Determine the friction losses for the given pipes. |
| 14. | Determine the loss of head coefficient for flow through pipes due to (i) sudden enlargement (ii) sudden contraction and (iii) bend(iv) Elbow |
| 15. | Determine the performance of the Kaplan turbine and draw the following Characteristic curves. Speed vs output power Speed vs Efficiency |
| 16. | Determine the performance of the Francis turbine and draw the constant head characteristic curves. |
| 17. | Determine the performance of the Pelton turbine, specific speed of the pump and draw the constant head Characteristic curves. |
| 18. | Determine the maximum efficiency and draw the performance characteristic curves by using Reciprocating Pump. |
| 19. | Determine the maximum efficiency of Roto-dynamic pumps (Centrifugal pump) and draw the following graphs Discharge vs Head Discharge vs input power Discharge vs efficiency |
| 20. | Determine the maximum efficiency of Gear Oil Pump and draw the following graphs Discharge vs Head Discharge vs input power Discharge vs efficiency |
| 21. | Determine the maximum efficiency and draw the performance characteristic curves by using submersible Pump. |

INTERNAL EXAMINER						 EXTERNAL EXAMINER