Roll No:

CIA TEST - I

Third Semester

Mechanical Engineering

ME3391 Engineering Thermodynamics

Date:   06.11.2023         	             					            Session    :  FN

Time:   1.30 Hrs                                                                                                          Maximum:  50 marks

Answer ALL Questions

PART - A (7 X 2 = 14 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 1 | State Clausius statement second law of thermodynamics. | 2 | CO2 | 1 | 2 |
| 2 | Express clausius inequality for various processes. | 2 | CO2 | 2 | 2 |
| 3 | What is difference between a heat pump and refrigerator? | 2 | CO2 | 2 | 1 |
| 4 | State carnot’s theorem | 2 | CO2 | 1 | 2 |
| 5 | What is the function of refrigerator? How is COP defined? | 2 | CO2 | 1 | 1 |
| 6 | Define Dryness fraction of Steam and Quality of steam. | 2 | CO4 | 1 | 2 |
| 7 | What is the laten heat of evaporation? | 2 | CO4 | 1 | 1 |

PART- B (3 X 12 = 36 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 11. | (a). A reversible heat engine operating between reservoirs at 900K and 300K drives a reversible refrigerator operating between reservoirs at 300K and 250K. The heat engine receives 1800 kJ heat from 900K reservoir. The net output from the combined engine refrigerator is 360kJ.Find the heat transferred to the refrigerator and the net heat rejected to the reservoir at 300K. | 12 | CO2 | 3 | 1 |
|  | Or |  |  |  |  |
|  | (b). A reversible engine operates between a source at 972ºC and two sinks, one at 127ºC and another at 27ºC. The energy rejected is same at both the sinks. What is the ratio of heat supplied to the heat rejected? Also calculate the efficiency. | 12 | CO2 | 5 | 1 |
| 12. | (a).Two Carnot engines A and B are operated in series. The first one (A) receives heat at 870 K and rejects heat to a reservoir at temperature T. The second engine (B) receives the heat rejected by the first engine and in turn rejects to a heat reservoir at 300K. Calculate the intermediate temperatures T in ºC between two heat engines for the following cases | 12 | CO2 | 3 | 2 |
|  | Or |  |  |  |  |
|  | (b). An engine is supplied with 1120 kJ/s of heat. The source and sink temperature are maintained at 560 K and 280 K. Determine whether the following cases represent the reversible, irreversible or impossible heat engines. (1) 900 kW of heat rejected (2) 560 kW of heat rejected (3) 108 kW of heat rejected | 12 | CO2 | 3 | 2 |
| 13. | (a).One kg of steam contains 1/3 liquid and 2/3 vapour by volume. The temperature of the steam is 150ºC. Find the quality, specific enthalpy of mixture | 12 | CO4 | 5 | 2 |
|  | Or |  |  |  |  |
|  | (b). A closed vessel of 0.2 m3 contains steam at 1 MPa and temperature 250ºC. If the vessel is cooled so that pressure falls to 350 kPa. Determine the final temperature, heat transfer, and change of entropy during the process. | 12 | C04 | 5 | 2 |

| BT LEVEL | CO2 | CO4 | % |
| --- | --- | --- | --- |
| Remember | Q. Nos | 1,2 | 5,6,7, | 11.62 |
|  | Marks | 04 | 06 |  |
| Understand | Q. Nos | 2,3 |  | 4.66 |
|  | Marks | 04 |  |  |
| Apply | Q.Nos | 11 (a), 12 (a), 12 (b) |  | 41.86 |
|  | Marks | 36 |  |  |
| Analyze | Q. Nos |  |  | - |
|  | Marks |  |  |  |
| Evaluate | Q. Nos | 11 (b) | 13 (a),13 (b) | 41.86 |
|  | Marks | 12 | 24 |  |
| Total | 56 | 30 | 100 |

| IQAC Member | HOD / Mech |
| --- | --- |