B.E / B.Tech. PRACTICAL END SEMESTER EXAMINATIONS, NOVEMBER / DECEMBER 2019

Fifth Semester

ME8513 - METROLOGY AND MEASUREMENTS LABORATORY

(Regulations 2017)

Time : 3 Hours			       Answer any one Question	                      Max. Marks 100

(To be filled by the question paper setter)

| Aim/Principle/Apparatus required/Procedure | Tabulation/Circuit/Program/Drawing | Calculation & Results | Viva-Voce | Record | Total |
| --- | --- | --- | --- | --- | --- |
| 25 | 25 | 30 | 10 | 10 | 100 |

| 1. | Calibrate the given micrometer in the range 0 – 25 mm using gauge blocks and determine the error involved in this range. |
| --- | --- |
| 2. | Calibrate the given Vernier calliper in the range 0 – 30 mm using gauge blocks and determine the error involved in this range. |
| 3. | Measure the height of given work piece by using Vernier height gauge. |
| 4. | Measure the depth of the given blind holes using depth gauge. Take 3 readings along the hole. |
| 5. | Determine the taper angle of the given component using slip gauges with sine bar. |
| 6. | Using gear tooth Vernier calliper, determine the chordal tooth thickness and depth of the given gear. |
| 7. | Determine the taper angle of the given component using sine bar. |
| 8. | Measure the major diameter of a given thread (Four threads of different diameter and pitch) using floating carriage micrometer. |
| 9. | Determine the following parameters in a screw thread using tool maker’s microscope - (i) minor diameter (ii) depth of thread (iii) pitch. |
| 10. | Measure the gear tooth thickness using gear tooth vernier caliper. |
| 11. | Checking the Limits of dimension of the given component using Mechanical Comparator |
| 12. | Determine the straightness along one edge of the machine tool guide way using autocollimator. |
| 13. | Determine the displacement of core using Linear variable differential Transducer. |
| 14. | What is the principle used in the force measurement setup available in your laboratory. Calibrate the force measurement setup, and plot a graph of error vs nominal force value. |
| 15. | Using the torque measuring setup measure the indicated torque and make a comparison with theoretical torque. |
| 16. | Use of CMM in metrology- Tracing the profile of a component and measurement of dimensions. |
| 17. | Measure the of Surface finish of the given component stylus based instruments. |
| 18. | Determine the maximum deviation from straightness for the machine tool slide using a reference line passing through the initial and final points, using autocollimator. |
| 19. | Measure the Bore diameter for a given specimen using bore gauge. |
| 20. | Measure the Bore diameter for a given specimen using telescope gauge. |