Roll No:

Sir Issac Newton College of Engineering and Technology-Nagapattinam

MODEL EXAM

Seventh Semester

Mechanical Engineering

ME8793 PROCESS PLANNING AND COST ESTIMATION

Date:    01.12.2022                        	             					 Session   :  FN

Time:  9.30am to 12.30 am                                         				Maximum:  100 marks

Answer ALL Questions

PART - A (10 X 2 = 20 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 1 | What is meant by processes planning? | 2 | CO1 | L1 | 2 |
| 2 | What are the materials selection parameters? | 2 | CO1 | L3 | 2 |
| 3 | List any six documents that are required for processes planning. | 2 | CO2 | L3 | 2 |
| 4 | What are the basic elements of jigs and fixtures? | 2 | CO2 | L2 | 2 |
| 5 | What are the different types of estimations? | 2 | CO3 | L4 | 2 |
| 6 | What do you meant by catalogue price? | 2 | CO3 | L1 | 2 |
| 7 | What are the various losses considered while calculating direct material cost for a casting? | 2 | CO4 | L4 | 2 |
| 8 | What are the various elements considered while calculating cost of a welded joints? | 2 | CO4 | L4 | 4 |
| 9 | What is meant by machining time? | 2 | CO5 | L2 | 4 |
| 10 | What is grinding? Different between surface and cylindrical grinding? | 2 | CO5 | L1 | 4 |

PART- B (5 X 15 = 65 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 11. | (a). What do you understand by CAPP? Explain in detail about the types of CAPP and Mention the benefits of CAPP? | 13 | CO1 | L2 | 2 |
|  | Or |  |  |  |  |
|  | (b). i. List out the factors that are common to both materials and process selection? ii. List and explain the various factors considered for tooling selection? | 7+6 | CO1 | L3 | 4 |
| 12. | (a). i. What are the set of documents that are required for process planning? ii. List and explain the various factors to be considered for selection measuring instruments? | 7+6 | CO2 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b). i. Explain the various principles of jigs and fixtures design? ii. What are two basic quality strategies? Explain them. | 7+6 | CO2 | L4 | 4 |
| 13. | (a). i. What are the different classification of cost? Explain? ii. Distinguish between estimating and costing? | 7+6 | CO3 | L3 | 2 |
|  | Or |  |  |  |  |
|  | (b). A factory is producing 1000 bolts and nuts per hour on a machine. Its material cost is Rs.400, labour cost. Rs.350 and direct expenses is Rs.75. The factory on cost is 150% of the total labour cost and office on cost is 25% of the total factory cost. If the selling price of each bolt and nut is Rs.1.75, calculate whether the factory is going in loss or gain and by what amount. | 13 | CO3 | L3 | 2 |
| 14. | (a). 200 pieces of the bolts are to be made from 25mm dia of rod. Find the length of each bolt before upsetting. What length of the rod is required if 3.5% of the length goes as scrap. | 13 | CO4 | L3 | 4 |
|  | Or |  |  |  |  |
|  | (b). Estimate the material cost for welding two flat pieces of MS 15x16x1cm size at an angle of 900 by gas welding. neglect edge preparation cost and assume cost of O2=Rs 15/m3 , cost of C2H2 =Rs 60/m2. Density of filler metal = 7gm/cc. cost of filler metal =Rs50/kg, filler rod diameter =5mm , filler rod required 4.5m/m of welding. Assume O2 consumption = 0.7 cu.m/hr. C2H2 consumption=0.5 cu.m/hr welding time=30min/m of welding. | 13 | CO4 | L3 | 4 |
| 15. | (a). A mild steel bar 120 mm long and 40 mm in diameter is turned to 38 mm diameter and was again turned to a diameter of 35 mm over a length of 50 mm as shown in fig. The bar was chamfered at both ends to give a chamfer of 45 *4 mm after facing. Calculate the machining time. Assume cutting speed of 50 m/min and feed 0.3 mm/rev. The depth of cut is not to exceed 3 mm in any operation. |  | CO5 | L3 | 2 |
|  | Or |  |  |  |  |
|  | (b). Estimate the planning time for a casting 1.25m long and 0.5m wide which is machined on a planer having cutting speed of 12m/min and a return speed of 30 m/min. two cuts are required: one roughing with a depth of 3.125 mm and a feed of 0.1mm/rev and other finishing with a depth of 0.125 mm and a using a feed of 0.125mm. |  | CO5 | L3 | 4 |

PART- C (1 X 15 = 15 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 16. | (a). Explain the Ladder diagram and cost estimating procedure ? | 15 | CO3 | L3 | 2 |
|  | Or |  |  |  |  |
|  | (b). Explain with an example about overhead costs and various bases used for absorption of overheads. | 15 | CO3 | L3 | 4 |

| BT LEVEL | CO1 | CO2 | CO3 | CO4 | CO5 | CO6 | % |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Remember | Q. Nos | 1 |  | 6 |  | 10 |  | 3.33 |
|  | Marks | 2 |  | 2 |  | 2 |  |  |
| Understand | Q. Nos | 11(A) | 4 |  |  | 9 |  | 9.44 |
|  | Marks | 13 | 2 |  |  | 2 |  |  |
| Applying | Q. Nos | 2, 11(B) | 3 | 13(A)13(B) 16(A) 16(B) | 14(A), 14(B) | 15(A) 15(B) |  | 69.44 |
|  | Marks | 15 | 2 | 56 | 26 | 26 |  |  |
| Analysing | Q. Nos |  | 12(A), 12(B) | 5 | 7,8 |  |  | 17.77 |
|  | Marks |  | 26 | 2 | 4 |  |  |  |
| Total | 30 | 30 | 60 | 30 | 30 |  | 100 |

| IQAC Member | HOD / Mech |
| --- | --- |