## Slide 1: PROJECTION OF PLANES
VEERAPANDIAN.K
AP/MECH
SINCET

## Slide 2
PROJECTIONS OF PLANES
In this topic various plane figures are the objects.
What will be given in the problem?
Description of the plane figure.
It’s position with HP and VP.
In which manner it’s position with HP & VP will be described?
1.Inclination of it’s SURFACE with one of the reference planes will be given.
2. Inclination of one of it’s EDGES with other reference plane will be given
(Hence this will be a case of an object inclined to both reference Planes.)
To draw their projections means F.V, T.V. & S.V.
What is usually asked in the problem?
Study the illustration showing
surface & side inclination given on next page.

## Slide 3
HP
a1
b1
c1
d1
VP
VP
a’
d’
c’
b’
VP
a’
d’
c’
b’
FV-3
T V-3
For Fv
For Tv
FV-1
T V-1
For F.V.
For T.V.
For T.V.
For F.V.
HP
a
b
c
d
a1’
d1’
c1’
b1’
HP
a1
b1
c1
d1
FV-2
T V-2
CASE OF A RECTANGLE – OBSERVE AND NOTE ALL STEPS.
SURFACE PARALLEL TO HP
PICTORIAL PRESENTATION
SURFACE INCLINED TO HP
PICTORIAL PRESENTATION
ONE SMALL SIDE INCLINED TO VP
PICTORIAL PRESENTATION
ORTHOGRAPHIC
TV-True Shape
FV- Line // to xy
ORTHOGRAPHIC
FV- Inclined to XY
TV- Reduced Shape
ORTHOGRAPHIC
FV- Apparent Shape
TV-Previous Shape
A
B
C

## Slide 4
PROCEDURE OF SOLVING THE PROBLEM:
IN THREE STEPS EACH PROBLEM CAN BE SOLVED:( As Shown In Previous Illustration )
STEP 1. Assume suitable conditions & draw Fv & Tv of initial position.
STEP 2. Now consider surface inclination & draw 2nd Fv & Tv.
STEP 3. After this,consider side/edge inclination and draw 3rd ( final) Fv & Tv.
ASSUMPTIONS FOR INITIAL POSITION:
(Initial Position means assuming surface // to HP or VP)
1.If in problem surface is inclined to HP – assume it // HP
Or If surface is inclined to VP – assume it // to VP
2. Now if surface is assumed // to HP- It’s TV will show True Shape.
And If surface is assumed // to VP – It’s FV will show True Shape.
3. Hence begin with drawing TV or FV as True Shape.
4. While drawing this True Shape –
keep one side/edge ( which is making inclination) perpendicular to xy line
( similar to pair no. on previous page illustration ).
A
B
Now Complete STEP 2. By making surface inclined to the resp plane & project it’s other view.
(Ref. 2nd pair on previous page illustration )
C
Now Complete STEP 3. By making side inclined to the resp plane & project it’s other view.
(Ref. 3nd pair on previous page illustration )
APPLY SAME STEPS TO SOLVE NEXT ELEVEN PROBLEMS

## Slide 5
X
Y
a
b
c
d
a’
b’
c’
d’
a1
b1
c1
d1
a1
b1
c1
d1
a’
b’
d’
c’
c’1
d’1
b’1
a’1
450
300
Problem 1:
Rectangle 30mm and 50mm sides is resting on HP on one small side which is 300 inclined to VP,while the surface of the plane makes 450 inclination with HP. Draw it’s projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------// to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? ---One small side.
Hence begin with TV, draw rectangle below X-Y
drawing one small side vertical.
Surface // to Hp
Surface inclined to Hp
Side
Inclined
to Vp

## Slide 6
Problem 2:
A 300 – 600 set square of longest side
100 mm long, is in VP and 300 inclined
to HP while it’s surface is 450 inclined
to VP.Draw it’s projections
(Surface & Side inclinations directly given)
Read problem and answer following questions
1 .Surface inclined to which plane? ------- VP
2. Assumption for initial position? ------// to VP
3. So which view will show True shape? --- FV
4. Which side will be vertical? ------longest side.
c1
X
Y
300
450
a’1
b’1
c’1
a
c
a’
a
b1
b’
b
a1
b
c
a’1
b’1
c’1
c’
Hence begin with FV, draw triangle above X-Y
keeping longest side vertical.
Surface // to Vp
Surface inclined to Vp
side inclined to Hp

## Slide 7
c
c1
X
Y
450
a’1
b’1
c’1
a
c
a’
a
b1
b’
b
a1
b
a’1
b’1
c’1
c’
35
10
Problem 3:
A 300 – 600 set square of longest side
100 mm long is in VP and it’s surface
450 inclined to VP. One end of longest
side is 10 mm and other end is 35 mm
above HP. Draw it’s projections
(Surface inclination directly given.
Side inclination indirectly given)
Read problem and answer following questions
1 .Surface inclined to which plane? ------- VP
2. Assumption for initial position? ------// to VP
3. So which view will show True shape? --- FV
4. Which side will be vertical? ------longest side.
Hence begin with FV, draw triangle above X-Y
keeping longest side vertical.
First TWO steps are similar to previous problem.
Note the manner in which side inclination is given.
End A 35 mm above Hp & End B is 10 mm above Hp.
So redraw 2nd Fv as final Fv placing these ends as said.

## Slide 8
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? -------- any side.
Hence begin with TV,draw pentagon below
X-Y line, taking one side vertical.
Problem 4:
A regular pentagon of 30 mm sides is resting on HP on one of it’s sides with it’s surface 450 inclined to HP.
Draw it’s projections when the side in HP makes 300 angle with VP
a’
b’
d’
b1
d
c1
a
c’e’
b
c
d1
b’1
a1
e’1
c’1
d’1
a1
b1
c1
d1
d’
a’
b’
c’e’
e1
e1
a’1
X
Y
450
300
e
SURFACE AND SIDE INCLINATIONS
ARE DIRECTLY GIVEN.

## Slide 9
Problem 5:
A regular pentagon of 30 mm sides is resting
on HP on one of it’s sides while it’s opposite
vertex (corner) is 30 mm above HP.
Draw projections when side in HP is 300 inclined to VP.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? --------any side.
Hence begin with TV,draw pentagon below
X-Y line, taking one side vertical.
b’
d’
a’
c’e’
a1
b1
c1
d1
e1
b1
c1
d1
a1
e1
b’1
e’1
c’1
d’1
a’1
X
Y
a’
b’
d’
c’e’
30
a
b
c
d
e
300
SURFACE INCLINATION INDIRECTLY GIVEN
SIDE INCLINATION DIRECTLY GIVEN:
ONLY CHANGE is
the manner in which surface inclination is described:
One side on Hp & it’s opposite corner 30 mm above Hp.
Hence redraw 1st Fv as a 2nd Fv making above arrangement.
Keep a’b’ on xy & d’ 30 mm above xy.

## Slide 10
450
300
a’
b’1
c’1
d’
a’
b’
d’
c’
a
c
b
d
a1
b1
c1
d1
b’
c’
a’1
d’1
d1
b1
c1
a1
X
Y
300
b’1
c’1
c1
a’1
d’1
d1
b1
c1
a1
450
a’
d’
a’
b’
d’
c’
a
c
b
d
a1
b1
d1
b’
c’
X
Y
TL
Problem 6: A rhombus of diagonals 40 mm and 70 mm long respectively has one end of it’s longer diagonal in HP while that diagonal is 350 inclined to HP. If the top-view of the same diagonal makes 400 inclination with VP, draw it’s projections.
Problem 7: A rhombus of diagonals 40 mm and 70 mm long respectively having one end of it’s longer diagonal in HP while that diagonal is 350 inclined to HP and makes 400 inclination with VP. Draw it’s projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diagonal horizontal? ---------- Longer
Hence begin with TV,draw rhombus below
X-Y line, taking longer diagonal // to X-Y
c2
The difference in these two problems is in step 3 only.
In problem no.6 inclination of Tv of that diagonal is
given,It could be drawn directly as shown in 3rd step.
While in no.7 angle of diagonal itself I.e. it’s TL, is
given. Hence here angle of TL is taken,locus of c1
Is drawn and then LTV I.e. a1 c1 is marked and
final TV was completed.Study illustration carefully.
Note the difference in
construction of 3rd step
in both solutions.

## Slide 11
T L
a
d
c
b
a’
b’
d’
c’
X
Y
a’
b’
d’
c’
a1
b1
d1
c1
a1
b1
d1
c1
450
300
a’1
b’1
c’1
d’1
a1
b1
d1
c1
a
d
c
b
a’
b’
d’
c’
a’
b’
d’
c’
a1
b1
d1
c1
300
a’1
b’1
c’1
d’1
Problem 8: A circle of 50 mm diameter is
resting on Hp on end A of it’s diameter AC
which is 300 inclined to Hp while it’s Tv
is 450 inclined to Vp.Draw it’s projections.
Problem 9: A circle of 50 mm diameter is
resting on Hp on end A of it’s diameter AC
which is 300 inclined to Hp while it makes
450 inclined to Vp. Draw it’s projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diameter horizontal? ---------- AC
Hence begin with TV,draw rhombus below
X-Y line, taking longer diagonal // to X-Y
The difference in these two problems is in step 3 only.
In problem no.8 inclination of Tv of that AC is
given,It could be drawn directly as shown in 3rd step.
While in no.9 angle of AC itself i.e. it’s TL, is
given. Hence here angle of TL is taken,locus of c1
Is drawn and then LTV I.e. a1 c1 is marked and
final TV was completed.Study illustration carefully.
Note the difference in
construction of 3rd step
in both solutions.

## Slide 12
Problem 10: End A of diameter AB of a circle is in HP
A nd end B is in VP.Diameter AB, 50 mm long is
300 & 600 inclined to HP & VP respectively.
Draw projections of circle.
The problem is similar to previous problem of circle – no.9.
But in the 3rd step there is one more change.
Like 9th problem True Length inclination of dia.AB is definitely expected
but if you carefully note - the the SUM of it’s inclinations with HP & VP is 900.
Means Line AB lies in a Profile Plane.
Hence it’s both Tv & Fv must arrive on one single projector.
So do the construction accordingly AND note the case carefully..
SOLVE SEPARATELY
ON DRAWING SHEET
GIVING NAMES TO VARIOUS
POINTS AS USUAL,
AS THE CASE IS IMPORTANT
TL
X
Y
300
600
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diameter horizontal? ---------- AB
Hence begin with TV,draw CIRCLE below
X-Y line, taking DIA. AB // to X-Y

## Slide 13
As 3rd step
redraw 2nd Tv keeping
side DE on xy line.
Because it is in VP
as said in problem.
X
Y
a
b
c
d
e
f
Problem 11:
A hexagonal lamina has its one side in HP and
Its apposite parallel side is 25mm above Hp and
In Vp. Draw it’s projections.
Take side of hexagon 30 mm long.
ONLY CHANGE is the manner in which surface inclination
is described:
One side on Hp & it’s opposite side 25 mm above Hp.
Hence redraw 1st Fv as a 2nd Fv making above arrangement.
Keep a’b’ on xy & d’e’ 25 mm above xy.
25
f’
e’
d’
c’
b’
a’
f’
e’
d’
c’
b’
a’
a1
b1
c1
d1
e1
f1
c1’
b’1
a’1
f’1
d’1
e’1
f1
a1
c1
b1
d1
e1
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diameter horizontal? ---------- AC
Hence begin with TV,draw rhombus below
X-Y line, taking longer diagonal // to X-Y

## Slide 14
A
B
C
H
H/3
G
X
Y
a’
b’
c’
g’
b a,g c
b a,g c
450
a’1
c’1
b’1
g’1
FREELY SUSPENDED CASES.
1.In this case the plane of the figure always remains perpendicular to Hp.
2.It may remain parallel or inclined to Vp.
3.Hence TV in this case will be always a LINE view.
4.Assuming surface // to Vp, draw true shape in suspended position as FV.
(Here keep line joining point of contact & centroid of fig. vertical )
5.Always begin with FV as a True Shape but in a suspended position.
AS shown in 1st FV.
IMPORTANT POINTS
Problem 12:
An isosceles triangle of 40 mm long
base side, 60 mm long altitude Is
freely suspended from one corner of
Base side.It’s plane is 450 inclined to
Vp. Draw it’s projections.
Similarly solve next problem
of Semi-circle
First draw a given triangle
With given dimensions,
Locate it’s centroid position
And
join it with point of suspension.