## Slide 1: SOLID PROJECTION
VEERAPANDIAN.K
AP/MECH
SINCET

## Slide 2
SOLIDS
To understand and remember various solids in this subject properly,
those are classified & arranged in to two major groups.
Group A
Solids having top and base of same shape
Cylinder
Prisms
Triangular Square Pentagonal Hexagonal
Cube
Triangular Square Pentagonal Hexagonal
Cone
Tetrahedron
Pyramids
( A solid having
six square faces)
( A solid having
Four triangular faces)
Group B
Solids having base of some shape
and just a point as a top, called apex.

## Slide 3
SOLIDS
Dimensional parameters of different solids.
Top
Rectangular
Face
Longer
Edge
Base
Edge
of
Base
Corner of base
Corner of base
Triangular
Face
Slant
Edge
Base
Apex
Square Prism
Square Pyramid
Cylinder
Cone
Edge
of
Base
Base
Apex
Base
Generators
Imaginary lines
generating curved surface
of cylinder & cone.
Sections of solids( top & base not parallel)
Frustum of cone & pyramids.
( top & base parallel to each other)

## Slide 4
X
Y
STANDING ON H.P
On it’s base.
RESTING ON H.P
On one point of base circle.
LYING ON H.P
On one generator.
(Axis perpendicular to Hp
And // to Vp.)
(Axis inclined to Hp
And // to Vp)
(Axis inclined to Hp
And // to Vp)
While observing Fv, x-y line represents Horizontal Plane. (Hp)
Axis perpendicular to Vp
And // to Hp
Axis inclined to Vp
And // to Hp
Axis inclined to Vp
And // to Hp
X
Y
F.V.
F.V.
F.V.
T.V.
T.V.
T.V.
While observing Tv, x-y line represents Vertical Plane. (Vp)
STANDING ON V.P
On it’s base.
RESTING ON V.P
On one point of base circle.
LYING ON V.P
On one generator.

## Slide 5
STEPS TO SOLVE PROBLEMS IN SOLIDS
Problem is solved in three steps:
STEP 1: ASSUME SOLID STANDING ON THE PLANE WITH WHICH IT IS MAKING INCLINATION.
( IF IT IS INCLINED TO HP, ASSUME IT STANDING ON HP)
( IF IT IS INCLINED TO VP, ASSUME IT STANDING ON VP)
IF STANDING ON HP - IT’S TV WILL BE TRUE SHAPE OF IT’S BASE OR TOP:
IF STANDING ON VP - IT’S FV WILL BE TRUE SHAPE OF IT’S BASE OR TOP.
BEGIN WITH THIS VIEW:
IT’S OTHER VIEW WILL BE A RECTANGLE ( IF SOLID IS CYLINDER OR ONE OF THE PRISMS):
IT’S OTHER VIEW WILL BE A TRIANGLE ( IF SOLID IS CONE OR ONE OF THE PYRAMIDS):
DRAW FV & TV OF THAT SOLID IN STANDING POSITION:
STEP 2: CONSIDERING SOLID’S INCLINATION ( AXIS POSITION ) DRAW IT’S FV & TV.
STEP 3: IN LAST STEP, CONSIDERING REMAINING INCLINATION, DRAW IT’S FINAL FV & TV.
AXIS
VERTICAL
AXIS
INCLINED HP
AXIS
INCLINED VP
AXIS
VERTICAL
AXIS
INCLINED HP
AXIS
INCLINED VP
AXIS TO VP
er
AXIS
INCLINED
VP
AXIS
INCLINED HP
AXIS TO VP
er
AXIS
INCLINED
VP
AXIS
INCLINED HP
GENERAL PATTERN ( THREE STEPS ) OF SOLUTION:
GROUP B SOLID.
CONE
GROUP A SOLID.
CYLINDER
GROUP B SOLID.
CONE
GROUP A SOLID.
CYLINDER
Three steps
If solid is inclined to Hp
Three steps
If solid is inclined to Hp
Three steps
If solid is inclined to Vp
Study Next Twelve Problems and Practice them separately !!
Three steps
If solid is inclined to Vp

## Slide 6
PROBLEM NO.1, 2, 3, 4 GENERAL CASES OF SOLIDS INCLINED TO HP & VP
PROBLEM NO. 5 & 6 CASES OF CUBE & TETRAHEDRON
PROBLEM NO. 7 CASE OF FREELY SUSPENDED SOLID WITH SIDE VIEW.
PROBLEM NO. 8 CASE OF CUBE ( WITH SIDE VIEW)
PROBLEM NO. 9 CASE OF TRUE LENGTH INCLINATION WITH HP & VP.
PROBLEM NO. 10 & 11 CASES OF COMPOSITE SOLIDS. (AUXILIARY PLANE)
PROBLEM NO. 12 CASE OF A FRUSTUM (AUXILIARY PLANE)
CATEGORIES OF ILLUSTRATED PROBLEMS!

## Slide 7
X
Y
a
b
c
d
o
o’
d’
c’
b’
a’
o’
d’
c’
b’
a’
o1
d1
b1
c1
a1
a’1
d’1
c’1
b’1
o’1
o1
d1
b1
c1
a1
o1
d1
b1
c1
a1
(APEX
NEARER
TO V.P).
(APEX
AWAY
FROM V.P.)
Problem 1. A square pyramid, 40 mm base sides and axis 60 mm long, has a triangular face on the ground and the vertical plane containing the axis makes an angle of 450 with the VP. Draw its projections. Take apex nearer to VP
Solution Steps :
Triangular face on Hp , means it is lying on Hp:
1.Assume it standing on Hp.
2.It’s Tv will show True Shape of base( square)
3.Draw square of 40mm sides with one side vertical Tv &
taking 50 mm axis project Fv. ( a triangle)
4.Name all points as shown in illustration.
5.Draw 2nd Fv in lying position I.e.o’c’d’ face on xy. And project it’s Tv.
6.Make visible lines dark and hidden dotted, as per the procedure.
7.Then construct remaining inclination with Vp
( Vp containing axis ic the center line of 2nd Tv.Make it 450 to xy as
shown take apex near to xy, as it is nearer to Vp) & project final Fv.
For dark and dotted lines
1.Draw proper outline of new view DARK. 2. Decide direction of an observer.
3. Select nearest point to observer and draw all lines starting from it-dark.
4. Select farthest point to observer and draw all lines (remaining)from it- dotted.

## Slide 8
Q Draw the projections of a pentagonal prism , base 25 mm side and axis 50 mm long, resting on one of its rectangular faces on the H.P. with the axis inclined at 45º to the V.P.
As the axis is to be inclined with the VP, in the first view it must be kept perpendicular to the VP i.e. true shape of the base will be drawn in the FV with one side on XY line
X
Y
a’ 1’
b’ 2’
c’ 3’
d’ 4’
e’ 5’
25
50
a
b
c
d
e
1
2
3
5
4
45º
a
b
c
d
e
1
2
3
5
4
a1’
b1’
c1’
d1’
e1’
11’
21’
31’
41’
51’

## Slide 9
Problem 2:
A cone 40 mm diameter and 50 mm axis
is resting on one generator on Hp
which makes 300 inclination with Vp
Draw it’s projections.
h
a
b
c
d
e
g
f
X
Y
a’
b’
d’
e’
c’
g’
f’
h’
o’
a’
h’b’
e’
c’g’
d’f’
o’
a1
h1
g1
f1
e1
d1
c1
b1
a1
c1
b1
d1
e1
f1
g1
h1
o1
a’1
b’1
c’1
d’1
e’1
f’1
g’1
h’1
o1
o1
30
Solution Steps:
Resting on Hp on one generator, means lying on Hp:
1.Assume it standing on Hp.
2.It’s Tv will show True Shape of base( circle )
3.Draw 40mm dia. Circle as Tv &
taking 50 mm axis project Fv. ( a triangle)
4.Name all points as shown in illustration.
5.Draw 2nd Fv in lying position I.e.o’e’ on xy. And
project it’s Tv below xy.
6.Make visible lines dark and hidden dotted,
as per the procedure.
7.Then construct remaining inclination with Vp
( generator o1e1 300 to xy as shown) & project final Fv.
For dark and dotted lines
1.Draw proper outline of new vie
DARK.
2. Decide direction of an observer.
3. Select nearest point to observer
and draw all lines starting from
it-dark.
4. Select farthest point to observer
and draw all lines (remaining)
from it- dotted.

## Slide 10
a b d c
1 2 4 3
X
Y
a b d c
1 2 4 3
a’
b’
c’
d’
1’
2’
3’
4’
450
4’
3’
2’
1’
d’
c’
b’
a’
4’
3’
2’
1’
d’
c’
b’
a’
350
a1
b1
c1
d1
1
2
3
4
Problem 3:
A cylinder 40 mm diameter and 50 mm axis is resting on one point of a base circle on Vp while it’s axis makes 450 with Vp and Fv of the axis 350 with Hp. Draw projections..
Solution Steps:
Resting on Vp on one point of base, means inclined to Vp:
1.Assume it standing on Vp
2.It’s Fv will show True Shape of base & top( circle )
3.Draw 40mm dia. Circle as Fv & taking 50 mm axis project Tv.
( a Rectangle)
4.Name all points as shown in illustration.
5.Draw 2nd Tv making axis 450 to xy And project it’s Fv above xy.
6.Make visible lines dark and hidden dotted, as per the procedure.
7.Then construct remaining inclination with Hp
( Fv of axis I.e. center line of view to xy as shown) & project final Tv.

## Slide 11
b
b1
X
Y
a
d
c
o
d’
c’
b’
a’
o’
d’
c’
b’
a’
o’
c1
a1
d1
o1
c1
b1
a1
d1
o1
o’1
a’1
b’1
c’1
d’1
Problem 4:A square pyramid 30 mm base side
and 50 mm long axis is resting on it’s apex on Hp,
such that it’s one slant edge is vertical and a
triangular face through it is perpendicular to Vp.
Draw it’s projections.
Solution Steps :
1.Assume it standing on Hp but as said on apex.( inverted ).
2.It’s Tv will show True Shape of base( square)
3.Draw a corner case square of 30 mm sides as Tv(as shown)
Showing all slant edges dotted, as those will not be visible from top.
4.taking 50 mm axis project Fv. ( a triangle)
5.Name all points as shown in illustration.
6.Draw 2nd Fv keeping o’a’ slant edge vertical & project it’s Tv
7.Make visible lines dark and hidden dotted, as per the procedure.
8.Then redrew 2nd Tv as final Tv keeping a1o1d1 triangular face
perpendicular to Vp I.e.xy. Then as usual project final Fv.

## Slide 12
Problem 5: A cube of 50 mm long edges is so placed on Hp on one corner that a body diagonal is
parallel to Hp and perpendicular to
Vp Draw it’s projections.
X
Y
b
c
d
a
a’
d’
c’
b’
a’
d’
c’
b’
a1
b1
d1
c1
a1
b1
d1
c1
1’
p’
p’
a’1
d’1
c’1
d’1
Solution Steps:
1.Assuming standing on Hp, begin with Tv,a square with all sides
equally inclined to xy.Project Fv and name all points of FV & TV.
2.Draw a body-diagonal joining c’ with 3’( This can become // to xy)
3.From 1’ drop a perpendicular on this and name it p’
4.Draw 2nd Fv in which 1’-p’ line is vertical means c’-3’ diagonal
must be horizontal. .Now as usual project Tv..
6.In final Tv draw same diagonal is perpendicular to Vp as said in problem.
Then as usual project final FV.
1’
3’
1’
3’

## Slide 13
Y
Problem 6:A tetrahedron of 50 mm long edges is resting on one edge on Hp while one triangular face containing this edge is vertical and 450 inclined to Vp. Draw projections.
X
T L
a
o
b
c
b’
a’
c’
o’
a’
a1
c1
o1
b1
a1
o1
b1
900
450
c1
c’1
b’
c’
o’
a’1
o’1
b’1
IMPORTANT:
Tetrahedron is a
special type
of triangular
pyramid in which
base sides &
slant edges are
equal in length.
Solid of four faces.
Like cube it is also
described by One
dimension only..
Axis length
generally not given.
Solution Steps
As it is resting assume it standing on Hp.
Begin with Tv , an equilateral triangle as side case as shown:
First project base points of Fv on xy, name those & axis line.
From a’ with TL of edge, 50 mm, cut on axis line & mark o’
(as axis is not known, o’ is finalized by slant edge length)
Then complete Fv.
In 2nd Fv make face o’b’c’ vertical as said in problem.
And like all previous problems solve completely.

## Slide 14
FREELY SUSPENDED SOLIDS:
Positions of CG, on axis, from base, for different solids are shown below.
H
H/2
H/4
GROUP A SOLIDS
( Cylinder & Prisms)
GROUP B SOLIDS
( Cone & Pyramids)
CG
CG

## Slide 15
X
Y
a’
d’
e’
c’
b’
o’
a
b
c
d
e
o
g’
H/4
H
LINE d’g’ VERTICAL
a’
b’
c’
d’
o”
e’
g’
a1
b1
o1
e1
d1
c1
a”
e”
d”
c”
b”
FOR SIDE VIEW
Problem 7: A pentagonal pyramid
30 mm base sides & 60 mm long axis,
is freely suspended from one corner of
base so that a plane containing it’s axis
remains parallel to Vp.
Draw it’s three views.
IMPORTANT:
When a solid is freely
suspended from a
corner, then line joining point of contact & C.G. remains vertical.
( Here axis shows inclination with Hp.)
So in all such cases, assume solid standing on Hp initially.)
Solution Steps:
In all suspended cases axis shows inclination with Hp.
1.Hence assuming it standing on Hp, drew Tv - a regular pentagon,corner case.
2.Project Fv & locate CG position on axis – ( ¼ H from base.) and name g’ and
Join it with corner d’
3.As 2nd Fv, redraw first keeping line g’d’ vertical.
4.As usual project corresponding Tv and then Side View looking from.

## Slide 16
a’
d’
c’
b’
b
c
d
a
a’
d’
c’
b’
a1
b1
d1
c1
d’’
c’’
a’’
b’’
X
Y
1’
1’
1’
Problem 8:
A cube of 50 mm long edges is so placed
on Hp on one corner that a body diagonal
through this corner is perpendicular to Hp
and parallel to Vp Draw it’s three views.
Solution Steps:
1.Assuming it standing on Hp begin with Tv, a square of corner case.
2.Project corresponding Fv.& name all points as usual in both views.
3.Join a’1’ as body diagonal and draw 2nd Fv making it vertical (I’ on xy)
4.Project it’s Tv drawing dark and dotted lines as per the procedure.
5.With standard method construct Left-hand side view.
( Draw a 450 inclined Line in Tv region ( below xy).
Project horizontally all points of Tv on this line and
reflect vertically upward, above xy.After this, draw
horizontal lines, from all points of Fv, to meet these
lines. Name points of intersections and join properly.
For dark & dotted lines
locate observer on left side of Fv as shown.)

## Slide 17
a1
h1
f1
e1
d1
c1
b1
g1
1
o1
400
Axis Tv Length
Axis Tv Length
Axis True Length
Locus of
Center 1
c’1
a’1
b’1
e’1
d’1
h’1
f’1
g’1
o’1
h
a
b
c
d
e
g
f
y
X
a’
b’
d’
e’
c’
g’
f’
h’
o’
a’
h’b’
e’
c’g’
d’f’
o’
450
a1
h1
f1
e1
d1
c1
b1
g1
o1
1
Problem 9: A right circular cone,
40 mm base diameter and 60 mm
long axis is resting on Hp on one
point of base circle such that it’s
axis makes 450 inclination with
Hp and 400 inclination with Vp.
Draw it’s projections.
This case resembles to problem no.7 & 9 from projections of planes topic.
In previous all cases 2nd inclination was done by a parameter not showing TL.Like
Tv of axis is inclined to Vp etc. But here it is clearly said that the axis is 400 inclined
to Vp. Means here TL inclination is expected. So the same construction done in those
Problems is done here also. See carefully the final Tv and inclination taken there.
So assuming it standing on HP begin as usual.

## Slide 18
450
(AVP 450 to Vp)
y1
X1
F.V.
T.V.
Aux.F.V.
X
Y
Problem 10: A triangular prism,
40 mm base side 60 mm axis
is lying on Hp on one rectangular face
with axis perpendicular to Vp.
One square pyramid is leaning on it’s face
centrally with axis // to vp. It’s base side is
30 mm & axis is 60 mm long resting on Hp
on one edge of base.Draw FV & TV of
both solids.Project another FV
on an AVP 450 inclined to VP.
Steps :
Draw Fv of lying prism
( an equilateral Triangle)
And Fv of a leaning pyramid.
Project Tv of both solids.
Draw x1y1 450 inclined to xy
and project aux.Fv on it.
Mark the distances of first FV
from first xy for the distances
of aux. Fv from x1y1 line.
Note the observer’s directions
Shown by arrows and further
steps carefully.

## Slide 19
X
Y
X1
Y1
o’
o
Fv
Tv
Aux.Tv
(AIP 450 to Hp)
450
Problem 11:A hexagonal prism of
base side 30 mm longand axis 40 mm long,
is standing on Hp on it’s base with
one base edge // to Vp.
A tetrahedron is placed centrally
on the top of it.The base of tetrahedron is
a triangle formed by joining alternate corners
of top of prism..Draw projections of both solids.
Project an auxiliary Tv on AIP 450 inclined to Hp.
TL
a’
b’
d’
c’
e’
f’
a
b
c
d
e
f
STEPS:
Draw a regular hexagon as Tv of
standing prism With one side // to xy
and name the top points.Project it’s Fv –
a rectangle and name it’s top.
Now join it’s alternate corners
a-c-e and the triangle formed is base
of a tetrahedron as said.
Locate center of this triangle
& locate apex o
Extending it’s axis line upward
mark apex o’
By cutting TL of edge of tetrahedron
equal to a-c. and complete Fv
of tetrahedron.
Draw an AIP ( x1y1) 450 inclined to xy
And project Aux.Tv on it by using similar
Steps like previous problem.
a1
b1
c1
d1
e1
f1
o1

## Slide 20
X
Y
X1
Y1
TL
AIP // to slant edge
Showing true length
i.e. a’- 1’
a’ b’ e’ c’ d’
1’ 2’5’ 3’4’
Fv
Tv
Aux.Tv
1
2
3
4
5
a
b
d
c
e
1
2
3
4
5
b1
c1
d1
e1
a1
Problem 12: A frustum of regular hexagonal pyrami is standing on it’s larger base
On Hp with one base side perpendicular to Vp.Draw it’s Fv & Tv.
Project it’s Aux.Tv on an AIP parallel to one of the slant edges showing TL.
Base side is 50 mm long , top side is 30 mm long and 50 mm is height of frustum.

## Slide 21
450
300
a1
b2
c3
d4
a’b’
c’d’
1’2’
3’4’
a’b’
1’2’
3’4’
a1
b1
c’d’
c1
d1
21
31
41
11
11’
11
21
41
a1
d1
31
b1
c1
21’
31’
41’
a1’
b1’
c1’
d1’

## Slide 22
Q13.22: A hexagonal pyramid base 25 mm side and axis 55 mm long has one of its slant edge on the ground. A plane containing that edge and the axis is perpendicular to the H.P. and inclined at 45º to the V.P. Draw its projections when the apex is nearer to the V.P. than the base.
X
Y
a
b
c
d
e
f
a’
b’ f’
c’ e’
d’
o
o’
a’
b’ f’
c’ e’
d’
o’
a1
b1
c1
d1
e1
f1
o1
The inclination of the axis is given indirectly in this problem. When the slant edge of a pyramid rests on the HP its axis is inclined with the HP so while deciding first view the axis of the solid must be kept perpendicular to HP i.e. true shape of the base will be seen in the TV. Secondly when drawing hexagon in the TV we have to keep the corners at the extreme ends.
45º
o1’
d1’
e1’
c1’
f1’
b1’
a1’
The vertical plane containing the slant edge on the HP and the axis is seen in the TV as o1d1 for drawing auxiliary FV draw an auxiliary plane X1Y1 at 45º from d1o1 extended. Then draw projectors from each point i.e. a1 to f1 perpendicular to X1Y1 and mark the points measuring their distances in the FV from old XY line.
X1
Y1