Roll No:

Sir Issac Newton College of Engineering and Technology-Nagapattinam

CIA TEST - I

Fifth  Semester

Mechanical Engineering

ME8595 THERMAL ENGINEERING II

Date: 29/09/2022  		             						  Session    :  FN

Time:  9.30am to 11.00 am                                         				Maximum:  50 marks

Answer ALL Questions

PART - A (5 X 2 = 10 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 1 | Define critical pressure ratio. | 2 | CO1 | L1 | 9 |
| 2 | Define nozzle. | 2 | CO1 | L1 | 9 |
| 3 | State the purpose of boiler testing and trial. | 2 | CO2 | L2 | 9 |
| 4 | State the importants of fusible plug. | 2 | CO2 | L1 | 9 |
| 5 | Define boiler mountings and accessories | 2 | CO2 | L1 | 9 |

PART- B (4 X 10 = 40 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 11. | (a). The inlet condition of steam nozzle is 10 bar and 2700 C. The exit pressure is 2 bar. Assuming isentropic expansion and negligible inlet velocity, determine the (i) throat area, (ii) exit velocity and (iii) exit area of the nozzle for a flow rate of 0.3 kg/s. | 10 | CO1 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b). Dry saturated steam at 2.8 bar is expanded through a convergent nozzle to 1.8 bar. The exit area is 3 cm2. Calculate the exit velocity and mass flow rate for (i) isentropic expansion and (ii) supersaturated flow. | 10 | CO1 | L4 | 2 |
| 12. | (a). A convergent- divergent adiabatic steam nozzle is supplied with steam at 10 bar and 3000 C. The discharge pressure is 1.2 bar. Assuming that the nozzle efficiency is 100% and initial velocity of steam is 50m/s, find the discharge velocity. | 10 | CO1 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b). Explain the any one high pressure boiler in detail. | 10 | CO2 | L1 | 9 |
| 13. | (a). Steam initially dry and saturated is expanded in a nozzle from 15 bar 290°C at 2 bar. if the friction loss in the nozzle is 12% of the total head drop calculate the mass of steam discharged when exit diameter of the nozzle is 20 mm. | 10 | CO1 | L2 | 2 |
|  | Or |  |  |  |  |
|  | (b). Dry saturated steam at a pressure of 10 bar enters a convergent-divergent nozzle and leaves at a pressure of 3 bar. If the flow is adiabatic and frictionless, determine the: Exit velocity of steam Ratio of cross-section of exit and that at throat. | 10 | CO2 | L2 | 2 |
| 14. | (a). Sketch and explain the economizer and super heater. | 10 | CO2 | L1 | 9 |
|  | Or |  |  |  |  |
|  | (b). Sketch and explain the Lamont boiler. | 10 | CO2 | L1 | 9 |

| BT LEVEL | CO1 | CO2 | CO3 | CO4 | CO5 | CO6 | % |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Remember | Q. Nos | 1,2 | 4,5,12a, 14a,14b |  |  |  |  | 42.2 |
|  | Marks | 4 | 34 |  |  |  |  |  |
| Understand | Q. Nos | 13a | 3,13b |  |  |  |  | 24.44 |
|  | Marks | 10 | 12 |  |  |  |  |  |
| Applying | Q. Nos |  |  |  |  |  |  |  |
|  | Marks |  |  |  |  |  |  |  |
| Analysing | Q. Nos | 11a,11b,12a |  |  |  |  |  | 33.33 |
|  | Marks | 30 |  |  |  |  |  |  |
| Total |  |  |  |  |  |  | 100 |

| IQAC Member | HOD / Mech |
| --- | --- |