Roll No:

Sir Issac Newton College of Engineering and Technology-Nagapattinam

CIA TEST - I

Fifth  Semester

Mechanical Engineering

ME8595 THERMAL ENGINEERING II

Date: 29/09/2022  		             						  Session    :  FN

Time: 9.30am to 11.00 am                                         				Maximum:  50 marks

Answer ALL Questions

PART - A (5 X 2 = 10 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 1 | Draw the various types of nozzle. | 2 | CO1 | L1 | 9 |
| 2 | Define nozzle efficiency. | 2 | CO1 | L1 | 9 |
| 3 | Define fusible plug. | 2 | CO2 | L1 | 9 |
| 4 | State the functions of water level indicator. | 2 | CO2 | L1 | 9 |
| 5 | Draw the economizer. | 2 | CO2 | L3 | 9 |

PART- B (4 X 10 = 40 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 11. | (a). Steam initially dry and saturated is expanded in a nozzle from 15 bar 300°C at 1 bar. if the friction loss in the nozzle is 12% of the total head drop calculate the mass of steam discharged when exit diameter of the nozzle is 15 mm. | 10 | CO1 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b). Air enters a frictionless adiabatic converging nozzle at 10 bar 500 K with negligible velocity. The nozzle discharges to a region at 2 bar. If the exit area of the nozzle is 2.5 cm2, find the flow rate of air through the nozzle. Assume for air Cp = 1005 J/kg K and Cv= 718 J/kg K. | 10 | CO1 | L4 | 2 |
| 12. | (a). The inlet condition of steam nozzle is 10 bar and 2500 C. The exit pressure is 2 bar. Assuming isentropic expansion and negligible inlet velocity, determine the (i) throat area, (ii) exit velocity and (iii) exit area of the nozzle for a flow rate of 0.2 kg/s. | 10 | CO1 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b). A convergent divergent adiabatic steam nozzle is supplied with steam at 10 bar and 250°c.the discharge pressure is 1.2 bar.assuming that the nozzle efficiency is 100% and initial velocity of steam is 50 m/s. find the discharge velocity. | 10 | CO1 | L3 | 2 |
| 13. | (a). Explain the any one low pressure boiler in detail. | 10 | CO2 | L2 | 8 |
|  | Or |  |  |  |  |
|  | (b). Sketch and explain the Benson boiler. | 10 | CO2 | L2 | 2 |
| 14. | (a). Sketch and explain any three boiler mountings. | 10 | CO2 | L1 | 8 |
|  | Or |  |  |  |  |
|  | (b). Sketch and explain the Loeffler boiler. | 10 | CO2 | L1 | 9 |

| BT LEVEL | CO1 | CO2 | CO3 | CO4 | CO5 | CO6 | % |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Remember | Q. Nos | 1,2 | 3,4,14a,14b |  |  |  |  | 31.11 |
|  | Marks | 4 | 24 |  |  |  |  |  |
| Understand | Q. Nos |  | 13a,13b |  |  |  |  | 22.22 |
|  | Marks |  | 20 |  |  |  |  |  |
| Applying | Q. Nos | 12b | 5 |  |  |  |  | 13.33 |
|  | Marks | 10 | 2 |  |  |  |  |  |
| Analysing | Q. Nos | 11a,11b,12a |  |  |  |  |  | 33.33 |
|  | Marks | 30 |  |  |  |  |  |  |
| Total |  |  |  |  |  |  | 100 |

| IQAC Member | HOD / Mech |
| --- | --- |