Roll No:

Sir Issac Newton College of Engineering and Technology-Nagapattinam

CIA TEST - II

Fifth  Semester

Mechanical Engineering

ME8595 THERMAL ENGINEERING II

Date :				             						  Session    :  FN

Time: 9.30am to 11.00 am                                         				Maximum  :  50 marks

Answer ALL Questions

PART - A (5 X 2 = 10 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 1 | What is the operating principle of reaction turbine? | 2 | CO3 | L1 | 9 |
| 2 | Define blade velocity coefficient in impulse turbine. | 2 | CO3 | L1 | 9 |
| 3 | Write about Wed Bulb Temperature. | 2 | CO5 | L2 | 9 |
| 4 | State the importants of air contioning. | 2 | CO5 | L1 | 9 |
| 5 | Define refrigeration and air contioning. | 2 | CO5 | L1 | 9 |

PART- B (4 X 10 = 40 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 11. | (a). The steam supply to an impulse turbine with a single row of moving blade is 3 kg/s. the turbine develops 150 KW, the blade velocity is being 150m/s. the steam flows from a nozzle with a velocity of 450 m/s and the coefficient of velocity of blade is 0.95. Find the nozzle angle, blade angle at entry and exit if the steam flows axially after passing over the blades. | 10 | CO3 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b). The velocity of steam leaving the nozzle of an impulse turbine is 900 m/s and the nozzle angle is 300. The blade velocity is 360 m/s and the blade velocity of coefficient is 0.84. assuming no of losses due to shock at inlet calculate for a mass flow of 1.5 kg/s and symmetrical blading (a) blade inlet angle (b) driving force on the wheel (c) axial thrust on the wheel and (d) power developed by the turbine. | 10 | CO3 | L4 | 2 |
| 12. | (a). The blade speed of a single ring impulse blading is 300 m/s and nozzle angle is 200. The heat drop is 625 KJ/kg and nozzle efficiency is 0.85. The blade discharge angle 300 and the machine develops 30 KW, when consuming 300 kg of steam per hour. Draw the velocity diagram and calculate the: 1) axial thrust on the blading and 2) heat equivalent per kg of steam friction of the blading. | 10 | CO3 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b). Steam enters the row of blades with a velocity of 320 m/s at an angle is of 270 with the direction of motion of moving blades. The velocity of steam passing over the blades is reduced by 12%. If the blade speed is 210 m/s, find the suitable inlet and outlet blade angle assuming that there is no thrust on blades. Also determine the power developed by the turbine per kg of steam flowing over the blades per second. | 10 | CO3 | L1 | 9 |
| 13. | (a). Air conditioning plant is required to supply 50 m3 of air per minute at a DBT of 22 0c and 50% RH. The atmospheric condition is 320c with 65% RH. Determine the mass of moisture removed and capacity of cooling coil if the required is obtained by dehumidification and sensible cooling process. Also calculate the sensible heat factor. | 10 | CO5 | L2 | 2 |
|  | Or |  |  |  |  |
|  | (b). Explain the winter and summer type AC with neat diagram. | 10 | CO5 | L2 | 2 |
| 14. | (a). Sketch and explain the vapour compression refrigeration system. | 10 | CO5 | L1 | 9 |
|  | Or |  |  |  |  |
|  | (b). Sketch and explain the Lithium Bromide water absorption system. | 10 | CO5 | L1 | 9 |

| BT LEVEL | CO1 | CO2 | CO3 | CO4 | CO5 | CO6 | % |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Remember | Q. Nos |  |  | 1,2, |  | 4,5, 14a,14b |  | 31.11 |
|  | Marks |  |  | 4 |  | 24 |  |  |
| Understand | Q. Nos |  |  |  |  | 3,13b |  | 13.33 |
|  | Marks |  |  |  |  | 12 |  |  |
| Applying | Q. Nos |  |  | 12a |  | 13a |  | 22.22 |
|  | Marks |  |  | 10 |  | 10 |  |  |
| Analysing | Q. Nos |  |  | 11a,11b, 12b |  |  |  | 33.33 |
|  | Marks |  |  | 30 |  |  |  |  |
| Total |  |  |  |  |  |  | 100 |

| IQAC Member | HOD / Mech |
| --- | --- |