Roll No:

Sir Issac Newton College of Engineering and Technology-Nagapattinam

CIA TEST - II

Fifth  Semester

Mechanical Engineering

ME8595 THERMAL ENGINEERING II

Date :				             						  Session    :  FN

Time: 9.30am to 11.00 am                                         				Maximum  :  50 marks

Answer ALL Questions

PART - A (5 X 2 = 10 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 1 | Define diagram efficiency. | 2 | CO3 | L1 | 9 |
| 2 | What you meant by compounding of turbine? | 2 | CO3 | L1 | 9 |
| 3 | Define refrigeration effect. | 2 | CO5 | L1 | 9 |
| 4 | Give the concept of cooling towers. | 2 | CO5 | L1 | 9 |
| 5 | Briefly write the necessity of refrigeration. | 2 | CO5 | L3 | 9 |

PART- B (4 X 10 = 40 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 11. | (a). A steam jet enters the row of blades with a velocity of 350 m/s at an angle is of 200 with the direction of motion of moving blades. The velocity of steam passing over the blades is reduced by 10%. If the blade speed is 200 m/s, find the suitable inlet and outlet blade angle assuming that there is no thrust on blades. Also determine the power developed by the turbine per kg of steam flowing over the blades per second. | 10 | CO3 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b). The velocity of steam leaving the nozzle of an impulse turbine is 1000 m/s and the nozzle angle is 200. The blade velocity is 350 m/s and the blade velocity of coefficient is 0.85. assuming no of losses due to shock at inlet calculate for a mass flow of 1.5 kg/s and symmetrical blading (a) blade inlet angle (b) driving force on the wheel (c) axial thrust on the wheel and (d) power developed by the turbine. | 10 | CO3 | L4 | 2 |
| 12. | (a). Steam enters the blade row of an impulse turbine with a velocity of 500 m/s at an angle of 300 to the plane of rotation of the blades. The mean blade speed is 280 m/s. the blade angle on the exit side is 350. The blade friction coefficient is 12%. Determine the Blade angle at inlet Work done per kg of stream Diagram efficiency Axial thrust per kg of steam per second. | 10 | CO3 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b). In a certain stage of an impulse turbine, the nozzle angle is 200 with the plane of the wheel. The mean diameter of the blading is 3 m. it develops 50 KW at 2500 rpm. Five nozzles, each of 10 mm diameters expands steam isentropically from 15 bar and 2500 C to 0.5 bar. The axial thrust is 3 N. calculate the 1) blade angle at entrance and exit and 2) power lost in blade friction. | 10 | CO3 | L3 | 2 |
| 13. | (a). The air enters a duct at 100C and 80% RH at the rate of 150 m3/min and is heated to 300C without adding or removing any moisture. The pressure remains constant at 1 bar. Determine the RH of air at exit from the duct and rate of heat transfer. | 10 | CO5 | L2 | 8 |
|  | Or |  |  |  |  |
|  | (b). Explain the WINTER AC and YEAR AROUND AC with neat diagram. | 10 | CO5 | L2 | 2 |
| 14. | (a). Explain the split type and summer type AC with neat diagram. | 10 | CO5 | L1 | 8 |
|  | Or |  |  |  |  |
|  | (b). With neat sketch explain the Water Vapour absorption Refrigeration system. | 10 | CO5 | L1 | 9 |

| BT LEVEL | CO1 | CO2 | CO3 | CO4 | CO5 | CO6 | % |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Remember | Q. Nos |  |  | 1,2, |  | 4,5, 14a,14b |  | 31.11 |
|  | Marks |  |  | 4 |  | 24 |  |  |
| Understand | Q. Nos |  |  |  |  | 3,13b |  | 13.33 |
|  | Marks |  |  |  |  | 12 |  |  |
| Applying | Q. Nos |  |  | 11a |  | 13a |  | 22.22 |
|  | Marks |  |  | 10 |  | 10 |  |  |
| Analysing | Q. Nos |  |  | 12a,11b, 12b |  |  |  | 33.33 |
|  | Marks |  |  | 30 |  |  |  |  |
| Total |  |  |  |  |  |  | 100 |

| IQAC Member | HOD / Mech |
| --- | --- |