Roll No:

Sir Issac Newton College of Engineering and Technology-Nagapattinam

MODEL EXAM

Fifth  Semester

Mechanical Engineering

ME8595 THERMAL ENGINEERING II

Date :	30.11.2022			             					  Session    :  FN

Time: 9.30am to 12.30 pm                                         				Maximum  :  100 marks

Answer ALL Questions

PART - A (10 X 2 = 20 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 1 | Draw the various types of nozzle. | 2 | CO1 | L1 | 9 |
| 2 | Define nozzle efficiency. | 2 | CO1 | L1 | 9 |
| 3 | State the functions of water level indicator. | 2 | CO2 | L1 | 9 |
| 4 | Draw the economizer. | 2 | CO2 | L3 | 9 |
| 5 | Define degree of reaction. | 2 | CO3 | L1 | 9 |
| 6 | Explain the need of compounding in steam turbines. | 2 | CO3 | L1 | 9 |
| 7 | State the factors influencing cogeneration. | 2 | CO4 | L2 | 8 |
| 8 | Define recuperator and regenerator. | 2 | CO4 | L2 | 8 |
| 9 | Give the concept of cooling towers. | 2 | CO5 | L1 | 9 |
| 10 | Briefly write the necessity of refrigeration. | 2 | CO5 | L3 | 9 |

PART- B (5X 13 = 65 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 11. | (a). A adiabatic CD steam nozzle is supplied with steam at 19 bar and 2500 C. The discharge pressure is 1.2 bar. Assuming that the nozzle efficiency is 100% and initial velocity of steam is 51m/s, find the discharge velocity. | 13 | CO1 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b). Air enters a frictionless adiabatic converging nozzle at 10 bar 500 K with negligible velocity. The nozzle discharges to a region at 2 bar. If the exit area of the nozzle is 2.5 cm2, find the flow rate of air through the nozzle. Assume for air Cp = 1005 J/kg K and Cv= 718 J/kg K. | 13 | CO1 | L4 | 2 |
| 12. | (a). Sketch and explain the Benson boiler. | 13 | CO2 | L2 | 2 |
|  | Or |  |  |  |  |
|  | (b) An Diesel engine uses 5 kg fuel having calorific value 44000 kJ/kg. in one hour. The brake power developed is 17kW. The temperature of 11.6 kg of cooling water found to rise through 25 0C per minute. The temperature of 4.1 kg of exhaust gas with specific heat 1 kJ/kg K was found to rise though 220 0C. Draw heat balance sheet for the engine. | 13 | CO2 | L3 | 9 |
| 13. | (a). A steam jet enters the row of blades with a velocity of 350 m/s at an angle is of 200 with the direction of motion of moving blades. The velocity of steam passing over the blades is reduced by 10%. If the blade speed is 200 m/s, find the suitable inlet and outlet blade angle assuming that there is no thrust on blades. Also determine the power developed by the turbine per kg of steam flowing over the blades per second. | 13 | CO3 | L4 | 2 |
|  | Or |  |  |  |  |
|  | (b) The velocity of steam leaving the nozzle of an impulse turbine is 1000 m/s and the nozzle angle is 200. The blade velocity is 350 m/s and the blade velocity of coefficient is 0.85. assuming no of losses due to shock at inlet calculate for a mass flow of 1.5 kg/s and symmetrical blading (a) blade inlet angle (b) driving force on the wheel (c) axial thrust on the wheel and (d) power developed by the turbine. | 13 | CO3 | L4 | 2 |
| 14. | (a) Explain the working of Kalina cycle and ORC plant with neat sketch. | 13 | CO4 | L2 | 2 |
|  | Or |  |  |  |  |
|  | (b) With a neat sketch. Explain the working of Ammonia Water “Neo- Gen” system . | 13 | CO4 | L3 | 2 |
| 15. | (a). The air enters a duct at 100C and 80% RH at the rate of 150 m3/min and is heated to 300C without adding or removing any moisture. The pressure remains constant at 1 bar. Determine the RH of air at exit from the duct and rate of heat transfer. | 13 | CO5 | L3 | 2 |
|  | Or |  |  |  |  |
|  | (b). Explain the split type and summer type AC with neat diagram. | 13 | CO5 | L2 | 9 |

PART- C (1 X 15 = 15 marks)

| 16. | (a). The inlet condition of steam nozzle is 10 bar and 2500 C. The exit pressure is 2 bar. Assuming isentropic expansion and negligible inlet velocity, determine the (i) throat area, (ii) exit velocity and (iii) exit area of the nozzle for a flow rate of 0.2 kg/s. | 15 | CO1 | L4 | 9 |
| --- | --- | --- | --- | --- | --- |
|  | Or |  |  |  |  |
|  | (b) Air conditioning plant is required to supply 60 m3 of air per minute at a DBT of 22 0c and 50% RH. The atmospheric condition is 300c with 65% RH. Determine the mass of moisture removed and capacity of cooling coil if the required is obtained by dehumidification and sensible cooling process. Also calculate the sensible heat factor. | 15 | CO5 | L4 | 9 |

| BT LEVEL | CO1 | CO2 | CO3 | CO4 | CO5 | CO6 | % |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Remember | Q. Nos | 1,2 | 3 | 5,6 |  | 9 |  | 6.66% |
|  | Marks | 4 | 2 | 4 |  | 2 |  |  |
| Understand | Q. Nos |  | 12(a) |  | 7,8,14(a) | 15(b) |  | 23.88% |
|  | Marks |  | 13 |  | 17 | 13 |  |  |
| Applying | Q. Nos | 16(a) | 4,12(b) |  | 14(b) | 10,15(a) |  | 32.22% |
|  | Marks | 15 | 15 |  | 13 | 15 |  |  |
| Analysing | Q. Nos | 11(a), 11(b), |  | 13(a), 13(b) |  | 16(b) |  | 37.22% |
|  | Marks | 26 |  | 26 |  | 15 |  |  |
| Total | 45 | 30 | 30 | 30 | 45 |  | 100 |

| IQAC Member | HOD / Mech |
| --- | --- |